## Slide 1: UNIT 3 Serial Port Programming
Asst. Prof Ravi U. Kalkundri

## Slide 2
The 8051 has two timers/counters, they can be used either as
  Timers to generate a time delay or as
  Event counters to count events happening outside the microcontroller.
Both Timer 0 and Timer 1 are 16 bits wide
  Since 8051 has an 8-bit architecture, each 16-bits timer is accessed as two separate registers of low byte and high byte

## Slide 3
  Accessed as low byte and high byte
  The low byte register is called TL0/TL1, and
  The high byte register is called TH0/TH1
  Accessed like any other register
    MOV TL0, #4FH
    MOV R5, TH0

## Slide 4
  Both timers 0 and 1 use the same register, called TMOD (timer mode), to set the various timer operation modes.
  TMOD is a 8-bit register
  The lower 4 bits are for Timer 0
  The upper 4 bits are for Timer 1
  In each case,
    The lower 2 bits are used to set the timer mode
    The upper 2 bits to specify the operation

## Slide 6
  Example 9-1
  Indicate which mode and which timer are selected for each of thefollowing.
  MOV TMOD, #01H (b) MOV TMOD, #20H (c) MOV TMOD, #12H
  Solution:
  We convert the value from hex to binary.
  (a) TMOD = 00000001, mode 1 of timer 0 is selected.
  (b) TMOD = 00100000, mode 2 of timer 1 is selected.
  (c) TMOD = 00010010, mode 2 of timer 0, and mode 1 of timer 1 are
  selected.

## Slide 7: Serial Port Programmng in C (continue..)
Example 10-16: Write a program for the 8051 to transfer “YES”serially at 9600 baud, 8-bit data, 1 stop bit, do this continuously
Solution:
  #include<reg51.h>
  void SerTx(unsigned char);
  void main(void)
  {
  TMOD,#20H; //timer 1,mode 2(auto reload)
  TH1,#-3; //9600 baud rate
  SCON,#50H; //8-bit, 1 stop, REN enabled
  TR1=1; //start timer 1
  while(1)
  {
    SerTx(‘Y’);
    SerTx(‘E’);
    SerTx(‘S’);
    }
    }
    void SerTx(unsigned char x)
    {
    SBUF=x;
    while(TI==0);
    TI=0;
    }

## Slide 8: Serial Port Programmng in C (continue..)
Example 10-17: Program the 8051 in C to receive bytes of data serially and put them in P1. Set the baud rate at 4800, 8-bit data, and 1 stop bit.
Solution:
#include <reg51.h>
void main(void){
unsigned char mybyte;
TMOD=0x20; //use Timer 1, mode 2
TH1=0xFA;` //4800 baud rate
SCON=0x50;
TR1=1; //start timer
while (1)
{ //repeat forever
  while (RI==0); //wait to receive
  mybyte=SBUF; //save value
  P1=mybyte; //write value to port
  RI=0;
}
}

## Slide 9: The steps that 8051 goes through in transmitting a character via TxD
The byte character to be transmitted is written into the SBUF register
The start bit is transferred
The 8-bit character is transferred on bit at a time
The stop bit is transferred
  It is during the transfer of the stop bit that 8051 raises the TI flag, indicating that the last character was transmitted
By monitoring the TI flag, we make sure that we are not overloading the SBUF.
  If we write another byte into the SBUF before TI is raised, the untransmitted portion of the previous byte will be lost
After SBUF is loaded with a new byte, the TI flag bit must be forced to 0 by CLR TI in order for this new byte to be transferred

## Slide 10: LCD Interfacing

## Slide 11: LCD Interfacing
LCD is very commonly used electronic display module and having a wide range of applications such as calculators, laptops, mobile phones etc.
16×2 character is very basic module which is commonly used in electronics devices and projects.
It can display 2 lines of 16 characters.
Each character is displayed using 5×7 or 5×10 pixel matrix.
LCD can be interfaced with microcontroller in 4 Bit or 8 Bit mode.
These differs in how data is sent to LCD.
In 8 bit mode to write a character, 8 bit ASCII data is sent through the data lines D0 – D7 and data strobe is given through EN of the LCD.
LCD commands which are also 8 bit are written to LCD in similar way.

## Slide 12: LCD Interfacing
4 Bit Mode uses only 4 data lines D4 – D7.
In this mode 8 bit character ASCII data and command data are divided into two parts and send sequentially through data lines.
The idea of 4 bit communication is used save pins of microcontroller.
4 bit communication is a bit slower than 8 bit communication but this speed difference can be neglected since LCDs are slow speed devices.
Thus 4 bit mode data transfer is most commonly used.

## Slide 13: LCD Interfacing

## Slide 14: LCD Interfacing
LCD Operations
LCD is finding widespread use replacing LEDs
The declining prices of LCD
The ability to display numbers, characters, and graphics
Incorporation of a refreshing controller into the LCD, thereby relieving the CPU of the task of refreshing the LCD
Ease of programming for characters and graphics

## Slide 15: LCD Interfacing (continue..)

## Slide 16: LCD Interfacing (continue..)

## Slide 17: ADCs (analog-to-digital converters)

## Slide 18: ADCs (analog-to-digital converters)
ADCs (analog-to-digital converters) are among the most widely used devices for data acquisition
  A physical quantity, like temperature, pressure, humidity, and velocity, etc., is converted to electrical (voltage, current) signals using a device called a transducer, or sensor.
We need an analog-to-digital converter to translate the analog signals to digital numbers, so microcontroller can read them

## Slide 19: ADCs (analog-to-digital converters)
ADC804 IC is an analog-to-digital converter
  It works with +5 volts and has a resolution of 8 bits
  Conversion time is another major factor in judging an ADC
    Conversion time is defined as the time it takes the ADC to convert the analog input to a digital (binary) number.
    In ADC804 conversion time varies depending on the clocking signals applied to CLK R and CLK IN pins, but it cannot be faster than 110 μs.

## Slide 20: ADCs (analog-to-digital converters)

## Slide 21: ADCs (analog-to-digital converters)
Block diagram of ADC

## Slide 22: ADCs (analog-to-digital converters)
  CLK IN and CLK R
  CLK IN is an input pin connected to an external clock source
  To use the internal clock generator (also called self-clocking), CLK IN and CLK R pins are connected to a capacitor and a resistor, and the clock frequency is determined by
    Typical values are R = 10K ohms and C = 150 pF
    We get f = 606 kHz and the conversion time is 110 μs

## Slide 23: ADCs (analog-to-digital converters)
Vref/2
It is used for the reference voltage
  If this pin is open (not connected), the analoginput voltage is in the range of 0 to 5 volts (the same as the Vcc pin)
  If the analog input range needs to be 0 to 4 volts, Vref/2 is connected to 2 volts

## Slide 24: ADCs (analog-to-digital converters)
D0-D7
  The digital data output pins
  These are tri-state buffered
    The converted data is accessed only when CS = 0 and RD is forced low
  To calculate the output voltage, use the following formula
    Dout = digital data output (in decimal),
    Vin = analog voltage, and
    step size (resolution) is the smallest change

## Slide 25: ADCs (analog-to-digital converters)
Analog ground and digital ground
  Analog ground is connected to the ground of the analog Vin.
  Digital ground is connected to the ground of the Vcc pin
To isolate the analog Vin signal from transient voltages caused by digital switching of the output D0 – D7
  This contributes to the accuracy of the digital data output

## Slide 26: ADCs (analog-to-digital converters)
The following steps must be followed for data conversion by the ADC804 chip
  Make CS = 0 and send a low-to-high pulse to pin WR to start conversion
  Keep monitoring the INTR pin
    If INTR is low, the conversion is finished
    If the INTR is high, keep polling until it goes low
  After the INTR has become low, we make CS = 0 and send a high-to-low pulse to the RD pin to get the data out of the ADC804

## Slide 27: ADCs (analog-to-digital converters)

## Slide 28: ADCs (analog-to-digital converters)
T1
T2
T3
T4
T5
T6

## Slide 29: Sensors
This section will show how to interface sensors to the microcontrollor.
Examine some popular sensors.

## Slide 30: Sensors
Temperature Sensor
Transducers convert physical data such as temperature, light intensity, flow and speed to electrical signals.
Depending on the transducer, the output produced is in the form of voltage, current or capacitance.
Eg: Temperature is converted to electrical signals using a transducer called Thermistor.

## Slide 31: Sensors
LM34 temperature sensors
The sensors of the LM34 series are precision integrated- circuit temperature sensors, whose Voltage output is linear proportional to the Fahrenheit temperature.
Requires no external calibration, as it is internally calibrated.
Output- 10mV for each degree of Fahrenheit temperature

## Slide 32: Sensors
LM34 temperature sensors
Part Scale | Temperature Range | Accuracy | Output
LM34A | -50 F to +300 F | +2.0 F | 10mV/F
LM34 | -50 F to +300 F | +3.0 F | 10mV/F
LM34CA | -40 F to +230 F | +2.0 F | 10mV/F
LM34C | -40 F to +230 F | +3.0 F | 10mV/F
LM34D | -32 F to +212 F | +4.0 F | 10mV/F
Table : LM34 Temperature Sensor Series Selection Guide

## Slide 33: Sensors
LM35 temperature sensors
The sensors of the LM34 series are precision integrated- circuit temperature sensors, whose Voltage output is linear proportional to the Celsius (centigrade) temperature.
Requires no external calibration, as it is internally calibrated.
Its outputs 10mV for each degree of centigrade temperature.

## Slide 34: Sensors
LM35 temperature sensors
Part | Temperature Range | Accuracy | Output
LM35A | -55 C to +150 C | + 1.0 C | 10mV/C
LM35 | -55 C to +150 C | + 1.5 C | 10mV/C
LM35CA | -40 C to +110 C | + 1.0 C | 10mV/C
LM35C | -40 C to +110 C | + 1.5 C | 10mV/C
LM35D | 0 C to +100 C | + 2.0 C | 10mV/C
Table : LM35 Temperature Sensor Series Selection Guide

## Slide 35: Sensors
Signal conditioning and interfacing the LM35 to the 8051
Signal conditioning is widely used in the world of data acquisition.
The most common transducers produce an output in the form of voltage, current charge, capacitance and resistance.
We need to convert these signals to voltages in order to send input to an A-to-D convertor.
This conversion is commonly called Signal Conditioning.
Signal Conditioning can be a current-to-voltage conversion or a signal amplification.
Analog world (temperature, pressure, etc )
Transducer
Signal conditioning
ADC
Microcontroller

## Slide 36: Sensors
//Program 13 – 2: C code to read temp from ADC0848, convert it to decimal, and put it on PO with some delay
#include <reg51.h>
sbit RD = P2^5;
sbit WR = P2^6;
sbit INTR = P2^7;
sfr MYDATA = P1; //P1 connected to DO-D7 of '848
void ConvertAndDisplay(unsigned char value) ;
void MSDelaylunsigned int value);
void main ()
{
MYDATA = OXFF; //make P1 and input
INTR =1; //make INTR and input
RD=1 // set RD high
WR=1; //set WR high
while(1)
{
WR=0; //send WR pulse
WR=1;
while(INTR = = 1); //wait for EOc
RD=0; //send RD pulse
value= MYDATA; // read vaue from ADCO848
ConvertAndDisplay (value);
RD=1;
}
}
void ConvertAndDisplay (unsigned char value)
{
unsigned char x, d1, d2,d3;
x=value/10;
d1=value%10;
d2=x%10;
d3=x/10;
P0=d1; //LSByte
MSDelay(250);
P0=d2;
MSDelay(250);
P0=d3; //MSByte
MSDelay(250);
}
void MSDelay(unsigned int value)
{
unsigned char x,y;
for(x=0;x<value;x++)
for(y=0;y<125;y++);
}