## Slide 1: Implementation of number system conversion
By:
2GI19CS157 Sumeet P Bafna
2GI19CS175 Venkatesh G Dhongadi 2GI19CS185 Vivek Raju Jadhav 2GI19CS186 Vivek Valagadde

## Slide 2: WHAT IS NUMBER SYSTEM…?
The number system that we use in our day-to-day life is the decimal number system

## Slide 3: CONVERSION AMONG BASES
The possibilities:
DECIMAL
OCTAL
BINARY
HEXADECIMAL

## Slide 4: BINARY TO DECIMAL
Technique :
  Multiply each bit by 2n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 5: EXAMPLE
1010112 => 1 x 20 = 1
1 x 21 = 2
0 x 22 = 0
1 x 23 = 8
0 x 24 = 0
1 x 25 = 32
4310
BIT “0”

## Slide 6: OCTAL TO DECIMAL
Technique
  Multiply each bit by 8n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 7: EXAMPLE
7248 => 4 x 80 = 4
2 x 81 = 16
7 x 82 = 448
46810

## Slide 8: HEXADECIMAL TO DECIMAL
Technique
  Multiply each bit by 16n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 9: EXAMPLE
ABC16 => C x 160 = 12 x 1 = 12
B x 161 = 11 x 16 = 176
A x 162 = 10 x 256 =2560
274810

## Slide 10: DECIMAL TO BINARY
Divide the decimal number with 2
Note the remainder
Do the above 2 steps for the quotient till the quotient is zero
Write the remainders in the reverse order.
The result is the required binary number.

## Slide 11: EXAMPLE
12510 => 2 125
2 62 1
2 31 0
2 15 1
2 7 1
2 3 1
2 1 1
0 1
12510 = 11111012

## Slide 12: HEXADECIMAL TO BINARY
Take given hexadecimal number
Find the number of digits in the decimal
If it has n digits, multiply each digit with 16n-1 where the digit is in the nth position
Add the terms after multiplication
The result is the decimal number equivalent to the given hexadecimal number.
Now covert the obtained decimal number to binary equivalent.

## Slide 13: EXAMPLE
(7D)16 => 7x161 = 7x16 = 112
Dx160 = 13x1 = 13
12510
Further Convert the obtained decimal number into binary equivalent as shown previously
12510 = 11111012
7D16 = 11111012

## Slide 14: OCTAL TO BINARY
Convert each octal digit to a 3-bit equivalent binary representation.

## Slide 15: EXAMPLE
5408 => 5->101
4->100
0->000
5408 = 1011000002

## Slide 16: OCTAL TO HEXADECIMAL
Convert the given octal number into binary equivalent.
Then convert the obtained binary number into hexadecimal equivalent.

## Slide 17: EXAMPLE
5368 = (101) (011) (110)= 1010111102
Now forming the group of 4 binary bits to obtain its hexadecimal equivalent,
1010111102= (0001) (0101) (1110)
= 15E16
5368 = 15E16

## Slide 18: THANK YOU