## Slide 1: PEDESTRIAN SAFETY
Presented by
Somanath Khot
Assistant Professor,
Department of Civil Engineering,
KLS GIT, Belagavi.

## Slide 2: Content:
Pedestrian - who?
Pedestrian Safety
Observations on Indian Roads
Design guidelines
Best Practices

## Slide 3: Pedestrian – Who?
Every person living on earth – a pedestrian
The World Health Organization (WHO, 2013) defines “A pedestrian is any person who is travelling by walking for at least part of his or her journey.
Various modifications and aids to walking such as wheelchairs, walkers, canes, skateboards, and roller blades.
The person may carry items of varying quantities, held in hands, strapped on the back, placed on the head, balanced on shoulders, or pushed/pulled along.
A person is also considered a pedestrian when running, jogging, hiking, or when sitting or lying down in the roadway.
Design of Pedestrian Facilities
3

## Slide 4: Pedestrian – Who?
A favourable environment for pedestrians would mean a favourable environment for ALL.
Street design has to answer inclusivity and accessibility for ALL
Walking is slowest of all other modes of transport, this slow pace has a lot of advantage as at this pace we can see distinguish between people, feel and understand the environment nearby.
Design of Pedestrian Facilities
4

## Slide 5: Pedestrian – Who?
In order to serve the above requirements and make walking a pleasurable experience there are 3 basic principles
  Coherence and directness,
  Attractiveness & comfort
  Safety & security
Walking is the basis of human movement, it is while walking we observe, connect, interact and learn
The benefits of walking can be classified into Economic, Environmental, Social and Health benefits, all of these benefits lead to a better quality of life for people
Design of Pedestrian Facilities
5

## Slide 6: WHY PEDESTRIAN SAFETY?
Urban sprawl has often left pedestrians stranded. Wide roads have been built without sidewalks or frequent crosswalks, and high-speed traffic makes these roadways particularly deadly.
In many areas, intersections with crosswalks may be as much as a kilometer apart, leaving pedestrians with no safe way to cross the street.

## Slide 7: Background - safety
Road accidents are a leading cause of death of young people between the age group of 10 – 24 years.(WHO)
In the year 2018 more than 2,00,000 people died in road crashes in India while the number of injured were about 5,43,000.
However, the actual number of injuries requiring hospital visits were 20,00,000 to 30,00,000
On average 40% of the total fatalities are pedestrian fatalities.
Design of Pedestrian Facilities
6

## Slide 10
0%
20%
60%
40%
80%
Driver
Pedestrian
MotorCycle Road Condition
Weather
Others
14%
1%
1%
2%
3%
1%
78%
Who’s Failure lead to an Accident
Cyclist
%age
0
80
60
40
20
Truck
Bus
Car
Taxi
Bicycle
Traffic Fatalities by Road User
Motorcycle
Mumbai
Pedestrian Delhi

## Slide 11: 350000
5000
pedestrians are killed
84000
pedestrians are injured
Every Year
Pedestrian accidents make up
11%
Of all motor vehicle accidents
Pedestrians were killed in motor vehicle accidents Between 1975 and 2018
60%
Of accidents occurred in Place where no crosswalks
88%
of accidents occurred in normal weather condition
64%
of accidents occurred at night

## Slide 12: Crash: Causes & Prevention
Inefficient Driver
Defective Vehicle
Bad Environment
Poor Operating Policies
Lack of Education
Inadequate Enforcement
Physical Roadway
Good engineering can reduce the effects of ...
Prevention

## Slide 13: Pedestrian crashes typically occur during the late afternoon and early evening hours presumably because of the reduced levels of visibility at a time when many people are on the road.

## Slide 14: Some observations on Indian Roads Current conditions
ON ROAD PARKING
30-40% of city roads are occupied with parking at any point of time

## Slide 15
road width
Walkway width = ??
Road width
street lighting, trees etc. are missing
Current conditions

## Slide 16
In-appropriate design of road cross sections- designed for nobody
Current conditions

## Slide 17
No designs at junctions- resulting in traffic bottlenecks and safety compromises
Current conditions

## Slide 18: “equitable space allocation for all road users with a focus on people rather than vehicles.”

## Slide 19
Current conditions

## Slide 20
Lady crossing the road
Lady Crossing Road Causes Fatal Road Accident _ Foolish

## Slide 21: BANGALORE
Rush Hour (on a 10m wide road)
Bike (1 PAX)
Car (1 PAX)
Bus (70 PAX)
1 KM of this road (No Buses)
  Approx. 300 cars & Bikes
  This reduces to only few buses if public transit to be used
But public transit itself is in poor condition
Congestion??

## Slide 22: ACCIDENTS (BANGALORE)
0
3750
7500
11250
15000
2003 2004 2005 2006 2007 2008 2009 2010 2011 2012 2013 (mid)
3052
5297
4767
5667
6138
6908
7469
6681
6782
8226
9662
487
735
727
816
737
864
957
880
796
875
843
Fatal
Non-Fatal

## Slide 23
Why Pedestrian Crossings Don’t Matter In India

## Slide 24: MITIGATION PLANS FOR PEDESTRAIN SAFETY
Safe infrastructure (walkways, over/under-pass etc)
Behavioral Issues (Traffic signs, Fines, Education, Culture)
Safety engineering (Optimum speed, designs etc.)

## Slide 25: Infrastructure for Pedestrian
Off-street facilities - Walkways
On-street Sidewalks/Footpath
Crosswalks
  Un-signalized
  Signalized
  Mid-block
Design of Pedestrian Facilities
9

## Slide 28: Guard Rails

## Slide 37: Footpaths
A footpath is the part of road or other public place that is laid out or built for pedestrian use.
Footpaths may run alongside the road or through parks and other open spaces, and include overbridges and subways.
Footways are those parts of access roads which are intended for use by pedestrians, and which generally are parallel with the carriageways and separated by curb.
Footpaths are those pedestrian routes which are located away from carriageways and not associated with routes of motor vehicles.
Design of Pedestrian Facilities
10

## Slide 38: Policy and design guidelines - India
National Urban Transport Policy (NUTP), 2006
National Mission on Sustainable Habitat (NMSH)
IRC Guidelines addressing pedestrians
  IRC: 103-2012 - Guidelines for pedestrian facilities
Institute for Transportation and Development Policy (ITDP), 2013
Design of Pedestrian Facilities
11

## Slide 39: Footpaths – Design goals
Provide footpaths wherever pedestrians will use them
Use footpath dimensions and geometry that provides access for all
Choose surface materials for safety, convenience and aesthetics
Manage design and location of street furniture
Locate and design driveways appropriately
Manage conflict on shared paths by good design and operation
Provide quality connections to public transport
Design of Pedestrian Facilities
39

## Slide 40: Footpaths – Design elements
Where to provide footpaths
Widths
Overhead and protrusion clearances
Gradient
Crossfall
Surfaces
Grates and covers
Landscaping
Street furniture
Ramps and steps
Driveways
Shared paths
Public transport interface
Design of Pedestrian Facilities
40

## Slide 41: Footpath standards (IRC 103-2012)
Design of Pedestrian Facilities
13

## Slide 42: Footpath standards (IRC 103-2012)
Design of Pedestrian Facilities
14

## Slide 43: Footpath standards (IRC 103-2012)
Footpaths are designed for level of service B and level service C (under resource constraint)
The width of the footpath should be designed based on expected pedestrian traffic
Design of Pedestrian Facilities
15
Side Design flow in number of pedestrians/hour walk In both directions In one direction width (m) LOS B LOS C LOS B LOS C |  |  |  | 
1.5 | 1350 | 1890 | 2025 | 2835
2.0 | 1800 | 2520 | 2700 | 3780
2.5 | 2250 | 3150 | 3325 | 4725
3.0 | 2700 | 3780 | 4050 | 5670
3.5 | 3150 | 4410 | 4725 | 6615
4.0 | 3600 | 5040 | 5400 | 7560

## Slide 44
Design of Pedestrian Facilities
17
Footpath standards (IRC 103-2012) - Kerb height
and surface quality
Kerb height should not exceed 150 mm
Even paved surfaces are important to people using sticks and wheel chairs
The gap between paving slabs should not exceed 5 mm

## Slide 45: Footpath standards (IRC 103-2012)
Footpaths should provide continuous space for walking of pedestrians
Bus stops, services, vendors, access to several types of properties, cross walks etc. are common on footpath
Well use of a footpath depends on successful integration of different footpath elements
Design of Pedestrian Facilities
18

## Slide 46
Design of Pedestrian Facilities
20
Access to properties (IRC 103-2012)

## Slide 47
Design of Pedestrian Facilities
21
Street Vending

## Slide 48: Tactile pavers (IRC 103-2012)
Design of Pedestrian Facilities
23
To guide the pedestrians with vision impairment
It is important that, whichever tactile pavers are
used for guiding or warning, they should be
used consistently used to avoid confusion.
Guide blocks indicate the correct route to follow , bus stops, property etc.
warning blocks to screen off the obstacles
Configuration of floor tactile paving
tactile paving to avoid obstacles

## Slide 49: Level of service
Design of Pedestrian Facilities
25

## Slide 50: Best practices
Design of Pedestrian Facilities
47

## Slide 51: Best practices
Design of Pedestrian Facilities
48

## Slide 52
Not This Way- Problem with Todays era of Technology???

## Slide 53: Case Study: Improvising a Junction for Pedestrian Movements in Mumbai Designing Streets like Pedestrians Matter_ HP Junction, Mumbai

## Slide 54: References:
IRC:103-2012 Guidelines for pedestrian facilities
PEDESTRIAN SAFETY–DESIGN by K Ramachandra Rao, Department of Civil Engineering and Transportation Research and Injury Prevention Program (TRIPP) Indian Institute of Technology, Delhi
PEDESTRIAN SAFETY by Ashish Samdariya and Achuth Vasudevan
Indian Express News Database

## Slide 55: Thank you
Design of Pedestrian Facilities
53